## Slide 1: Simulated GOLD Observations of Atmospheric Waves
John Correira1, J. Scott Evans1, Jerry D. Lumpe1,
Mihail Codrescu2, David W. Rusch3, Amal Chandran3,
Richard Eastes4, and the GOLD Science Team
Computational Physics, Inc.
NOAA Space Weather Prediction Center
Laboratory for Atmospheric and Space Physics, University of Colorado
Florida Space Institute, University of Central Florida
Notes: Acknowledge Dave & Amal for helping get early version of this effort started. Thank Mihail for providing CTIPe model results.
Ended up being more about ‘Simulated GOLD observations’ than ‘Atmospheric Waves’

## Slide 2: Overview
GOLD Day Disk Data
Simulations
L1C Data
Model O/N2
Level 2 Derived O/N2

## Slide 3: GOLD Disk Measurement Schedule
Spacecraft Local Time
Day Disk
24 minutes/scan
Limb
Occultation
Notes: 24 minutes per scan + 6 minutes for Occ or Limb = 30 minute cadence

## Slide 4: Simulations
Atmosphere
CTIPe
Ionosphere
IRI
AURIC
volume emission rates
LOSI_3D
database
AURIC N2 LBH model
L1C into data processing pipeline
Geolocation
SPICE
Simulated L2 files
Solar spectra
NRLEUV scaled by SEE
AURIC upper atmospheric radiance modeling from the FUV to the NIR [Strickland et al., 1999]
Also used for testing Level 2 pipeline and algorithm codes
GNU parallel allowed work to be distributed over 100 cores
L1C & L2 data will be NetCDF
LOS integration
Simulated L1C files
atomic emissions
Notes: Time varying solar spectra, can and will simulate flares
Note that LOSI_3D handles the atomic emissions

## Slide 5: O/N2 Algorithm
Ratio of column density of O above the altitude where the N2 column density is 1017 cm-2
Intensity ratio & SZA uniquely specifies O/N2
Inputs: 1356/LBH intensity ratio, uncertainties, SZA, look up table
Signature of atmospheric dynamics
GOLD spectral resolution allows for flexibility in choosing best LBH bands
Strickland, Evans, and Paxton, JGR, 100, A7, 1995

## Slide 6: Model O/N2
CTIPe results for 25 Oct 2015
  DOY 298
10 minute cadence
      Could use to implement time variation of atmosphere during course of single scan
18° longitude spacing
2° latitude spacing
Altitude range 75 km ~ 415 km

## Slide 7: Example L1C data
125 km x 125 km @ nadir
Hemispheres scanned separately
  Slit will overlap 1 degree at equator
  Both hemispheres included in L1C & L2 files
  Combined here
LBH roughly equivalent to GUVI LBH ‘Short’ (141 - 154 nm)
DOY 298, UT 1500, LT 1200
Notes: Note disk scan starts two steps off disk.
Two hemispheres not temporally coincident in real data.
Auroral emssions not included at this stage, will be included in the future (algorithms required an auroral contamination flag)
This is not pixelation of the image, this is the L1C grid

## Slide 8: Level 2 O/N2 data
250 km x 250 km @ nadir
  2x2 binning of Level 1C data
Constraints
  SZA < 80°
  Emission Angle < 75°
  Currently emission angle effects are not included in look up tables.

## Slide 9: Summary
Simulations will help demonstrate the feasibility of detecting various atmospheric phenomena.
Multi purpose
Test algorithms
Observation strategies
Provide realistic data processing pipeline codes
Future work
  Incorporate instrument
  Auroral emissions
  Solar flares
Notes: Simulated O/N2 suggest interesting features will be observable

## Slide 10: Extra Slides

## Slide 11: 1356 disk only

## Slide 12: 1356 with limb

## Slide 13: LBH disk only

## Slide 14: LBH with limb

## Slide 15: 1356/LBH Intensity Ratio